Embedded Serial-to-Ethernet Module

ATC-1000M （Rev2.0）

Pin Description

| Type | Description |
| --- | --- |
| I | Input pin. |
| O | Output pin. |
| IPL | Input pin with internal pull low. |
| IPH | Input pin with internal pull high. |
| P | Power supply. |
| N/C | No Connection. |

| Pin No | Label | Type | Description |
| --- | --- | --- | --- |
| 1,29 | GND | P | Ground |
| 2,17 | VCC3.3V | P | 3.3V supply voltage. |
| 3 | ADC_REFH | I | The upper reference voltage. The maximum input voltage range is determined by the voltage applied to ADC_REFH and the voltage applied to ADC_REFL. |
| 4 | ADC_REFL | I | The lower reference voltage. |
| 5 | ADC0 | I | ADC channel 0 analog input. |
| 6 | ADC1 | I | ADC channel 1 analog input. |
| 7 | RESETB | I | Reset, low active. This pin should be kept at “low” state for at least 10 microseconds. Connect this pin to a 1M ohms pull up resistor. There is an internal capacitor between this pin and GND, so the external capacitor is not necessary for a RC reset circuit. |
| 8 | LED_LINK | O | LINK_LED |
| 9 | HSRXD | I | TTL/CMOS driver input. |
| 10 | HSTXD | O | TTL/CMOS receiver output. |
| 11 | RTS | O | Request To Send Control Output / Handshake signal. |
| 12 | DTR | O | Data Terminal Ready Control Output / Handshake signal. |
| 13 | CTS | I | Clear to Send Control input / Handshake signal. |
| 14 | DSR | I | Data Set Ready Control Input / Handshake signal. |
| 15 | DCD | I | Data Carrier Detect Control input. |
| 16 | RI | I | Ring Indicator Control Input. |
| 18 | P1_2 | IPH/O | GPIO P1_2 |
| 19 | P3_0 | IPH/O | Restore the setting to factory default. This pin should be low at first, and then power on. Release it after three seconds. |
| 20 | P3_1 | IPH/O | Port3 is an 8-bit bidirectional I/O port. Port3 also provides various special features listed below: GPIO P3_1 or STXD0, serial output port 0 GPIO P3_2 GPIO P3_3 or INT1, External interrupt 1 GPIO P3_4 or T0, Timer 0 external input GPIO P3_5 or T1, Timer 1 external input |
| 21 | P3_2 |  |  |
| 22 | P3_3 |  |  |
| 23 | P3_4 |  |  |
| 24 | P3_5 |  |  |
| 25 | RX- | I | Ethernet receiver negative. |
| 26 | RX+ |  | Ethernet receiver positive. |
| 27 | TX+ | O | Ethernet transmitter positive. |
| 28 | TX- |  | Ethernet transmitter negative. |
| 30 | NC | N/C | No Connection. |

PIN Assignment:

Carrier Board Description:

# Text boxes

Specifications

Form Factor

Type: 30-pin dual-inline drop-in module

Pitch: 1.27mm

Dimensions: 37x27x12mm

Network Interface

Type: 10/100BaseT, auto-detect

Protocols: TCP, UDP, HTTP, Telnet, IP, ICMP, ARP

IP addressing: DHCP, Static IP

Operation Modes

TCP/Server, TCP/Client and UDP mode

Serial Interface (TTL-level)

Signals: TxD, RxD, RTS, CTS, DTR, DSR, DCD, GND

Baud: 300 to 230,400 bps

Parity: None, Even, Odd

Data bits: 7,8

Stop bit: 1,2

Flow control: None, RTS/CTS, XON/OFF

Programmable Digital I/O

PIO0~PIO6: TTL level compatible

Configuration Methods

Web console, Telnet Console and Serial Console

Windows utility (included in CD)

General

Power input: 3.3VDC

Power consumption: 350mA@+3.3VDC

Operation temp.: 0~70C, 5~95% RH

Storage temp.: -20~85C, 5~95% RH

Regulation: CE/FCC compliant

Warranty: 2 years

Description

- Adds Ethernet connectivity for RS-232/422/485 devices

- 10/100Mbps Ethernet; 230,400bps serial data rate

- Supports TCP/Server, TCP/Client and UDP mode

- Provides six TTL-level programmable digital I/Os

- Web/Telnet/Serial consoles for device configuration

- Windows utility included for device management

Dimensions

Order information:

ATC-1000M

Serial-to-Ethernet Embedded module

ATC-1000 EVB

Kit for ATC-1000M, including one ATC-1000M

module, one carrier board, one power adapter and

one CD-ROM with VSP driver.

Contact information:                                      Agent:

SHENZHEN ATC TECHNOLOGY CO., LTD

Room 809,Taikang Building,Tairan Industrial&Trading,

Futian District, Shenzhen China

E_mail: sales@szatc.com

Homepage: http://www.szatc.com

Contact information:

SHENZHEN ATC TECHNOLOGY CO., LTD

Room 809,Taikang Building,Tairan Industrial&Trading,

Futian District, Shenzhen China

E_mail: sales@szatc.com

Homepage: http://www.szatc.com